## Slide 1: Principal Concepts behind IBM Q D. Stancil, Quantum Computing CSC591/ECE592, 14 Oct. 2019
A. Blais, et al, “Cavity quantum electrodynamics for superconducting electrical circuits: An architecture for quantum computation,” Phys. Rev. A, Vol. 9, 062320 (2004)
J. Koch, et al, “Charge-insensitive qubit design derived from the Cooper Pair Box,” Phys. Rev. A Vol. 76, 042319 (2007).
J. Clarke & F. Wilhelm, “Superconducting quantum bits,” Nature, Vol. 453, 19 June 2008, p. 1031.
J.M. Chow, “Quantum Information Processing with Superconducting Qubits,” Ph.D. Dissertation, Yale Univ., 2010.
C.T. Rigetti, “Quantum Gates for Superconducting Qubits,” Ph.D. Dissertation, Yale Univ., 2009.
C. Rigetti and M. Devoret, “Fully microwave-tunable universal gates in superconducting qubits with linear couplings and fixed transition frequencies,” Phys. Rev. B vol. 81, 134507 (2010)
T. Van Duzer and C.W. Turner, “Principles of Superconductive Devices and Circuits,” Elsevier, 1981.
A. Kandala, A. Mezzacapo, K. Temme, M. Takita, M. Brink, J.M. Chow and J.M. Gambetta, “Hardware-efficient variational quantum eigensolver for small molecules and quantum magnets,” Nature, Vol. 549, p. 242 (2017).
D. C. McKay, C. J. Wood, S. Sheldon, J.M. Chow, and J. Gambetta, “Efficient Z gates for quantum computing,” Phys. Rev. A vol. 96, p. 022330 (2017).

## Slide 2: Outline
Requirements for a Quantum Computer
Quantum Mechanics of Two State Systems
Rotations
Creating Gates with Rabi Oscillations
Superconducting Qubits
  How to make qubits with circuits
  Superconductivity
  Josephson junction and nonlinear LC circuits
  SQUID: Tunable nonlinear inductance
  Transmon
Entangled transmons and controlled gates
IBM example chip layout

## Slide 3: (Subset of) Requirements for Quantum Computer (Paraphrase of DiVencenzo)
Physical system with two uniquely addressable states
A universal set of quantum gates
  Ability to implement arbitrary rotations on the Bloch sphere
  Ability to entangle two qubits
Ability to measure the state of a cubit

## Slide 4: Two State Systems in Quantum Mechanics

## Slide 5: Schrodinger Equation
H is an expression for the total energy of the system (kinetic + potential) and is called the Hamiltonian
For two orthogonal states:
What if we introduce a perturbation that weakly couples states 0 & 1?

## Slide 6: Schrodinger Equation for 2x2 coupled system
This can be written

## Slide 7: Prototypical 2-state system: Spin in a Magnetic Field
+
B
S

## Slide 8: Time Evolution of a Spin in a Magnetic Field
General solution:
Express coefficients in terms of a “mixing angle”:
Expectation of x spin component:

## Slide 9: Larmor Precession
A general superposition state precesses at the frequency of the energy difference between the two states
Measured spin must be described by normal rotation matrices, so it follows that the rotation operators on the state vector must be somewhat different

## Slide 10: Rotations

## Slide 11: Unitaries representing rotations
Within an arbitrary phase

## Slide 12: Arbitrary point on Bloch Sphere
Two rotations can take you from the ground state to any point on the Bloch sphere

## Slide 13: Most General 2x2 Unitary
In mechanics, 3 angles are needed to orient an object arbitrarily (e.g., roll, pitch, yaw)
Euler Angles Rotations: 12 different ways of defining the rotations and their order
ZYZ convention of particular interest since we will see that Z rotations can be performed with essentially no error

## Slide 14: Representations of most general 2x2 unitary
Or since an overall phase is not observable
Qiskit also defines

## Slide 15: Common gates realized with u3

## Slide 16: Creating Gates with Rabi Oscillations

## Slide 17: Creating Rotations: Rabi Oscillations
Suppose a time-varying field is applied along the x direction
The Hamiltonian becomes
Move to a frame rotating at
Note that rotating a state vector by  is equivalent to rotating the coordinates by -, so the state vector in the rotation frame is

## Slide 18: Hamiltonian in the Rotating Frame

## Slide 19: Rotating Wave Approximation
Putting the pieces together:
Neglect the frequency components near twice 0 since they will tend to average out: Rotating Wave Approximation
 = d - 0

## Slide 20: Time Evolution of State Vector in Rotating Frame
If the drive frequency matches the qubit frequency,  = 0.

## Slide 21: Example: Rotation About x Axis
Note that the rate of rotation can be controlled by varying either the amplitude or the phase of the microwave drive signal

## Slide 22: Realizing Gates using Rabi Oscillations
Recall that when driven at resonance
“-pulse”: inverts the state
“/2-pulse”: creates equal superposition of states
Key point: you can flip a state or create a superposition state by controlling the pulse length and/or amplitude & controlling the phase of the excitation
X gate: pi-pulse with
Y gate: pi-pulse with
Z gate: Rotations around the z axis can be accomplished simply by resetting the phase reference of the RF drive! Result: zero time and zero error (“Virtual Z Gate, VZ”)
x
y
z
This is a key point for an important error mitigation technique: Richardson extrapolation

## Slide 23: Superconducting Qubits

## Slide 24: Qubit possibility: LC Resonant Circuits?
In classical, linear circuit theory, the natural solution for the current is
The current can have any amplitude, independent of the frequency
Energy is stored alternately in the electric field of the capacitor and the magnetic field of the inductor, and can have any value
In reality, the stored energy is quantized
Could we use two of these states for a qubit, say n=0 and n=1?

## Slide 25: Nonlinear Resonant Circuits
Problem: energy difference between 0,1 is the same as energy difference between all other states n,n+1
  No way to address specific states
Solution: if either L or C were nonlinear (i.e., their values depended on the magnitude of the current or voltage), then the energy levels would no longer be equally spaced!
  If the energy difference between n=0 and n=1 is different from the energy difference from all other states, we can selectively address this particular transition by tuning the frequency of the applied excitation
Graphic: Clarke & Wilhelm
Graphic: http://hyperphysics.phy-astr.gsu.edu/hbase/quantum/hosc.html

## Slide 26: RF Frequency
The fact that we are talking about circuits suggests we are talking about RF rather than optical frequencies!
Problem: any physical mass at finite temperature will emit electromagnetic radiation that depends on its temperature (Black body radiation)
  We want the energy difference between qubit states to be large compared to thermal radiation
  Highest frequency for widespread, economical instrumentation ~ 6 GHz (owing, e.g., to WIFI, etc.)
  From kT=hf, the temperature corresponding to 6 GHz is 0.29K
  Operating temperature must be much less than 0.3K!
Solution: IBM Q systems operate at a temperature of about 15 mK using dilution refrigeration
Graphic: Wikipedia

## Slide 27: Superconductivity
At such low temperatures, metals such as Al and Nb become superconductors
  At low temperatures, an attractive force between electrons appears
  When this force gets sufficiently strong compared to thermal vibrations, electrons bind together into “Cooper pairs” with spin 1 and charge 2q
  Cooper pairs form a macroscopic quantum state enabling charge to move without scattering or loss, resulting in superconductivity
Makes it possible to realize extremely low-loss RF transmission lines
Makes it possible to realize a nonlinear inductor using a Josephson junction

## Slide 28: A note to Physicists: Cooper Pairs and Superconductivity
Spin ½ particles are “Fermions”
  Fermions obey the Pauli exclusion principle: no two can be in the same state
  Electrons are Fermions
Spin 1 particles are “Bosons”
  Bosons do not obey the Pauli exclusion principle: you can have as many in a state as you want
  Photons are Bosons
In a superconductor, an effective attractive interaction between electrons causes them to be loosely bound together and act like a single spin 1 particle: “Cooper Pair”
Since Cooper pairs are spin 1, they act like Bosons, and you can have multiple Cooper pairs in the same state
All of the Cooper pairs in a macroscopic sample can be in the same coherent state

## Slide 29: Cooper Pairs are the result of the Electron-Phonon interaction in the theory of Bardeen, Cooper, and Schreifer (BCS Theory)
Electrons normally repel one another, but are attracted to ions in the crystal lattice
If the ions are pulled slightly toward an electron, from a distance it can appear as though there is a net positive charge, attracting another electron

## Slide 30: Josephson tunnel junction
Two superconductors separated by a thin insulating layer
Wave functions for superconducting Cooper pairs decay exponentially in the insulating layer
If the layer is thin enough to allow appreciable tunneling, then phases are no longer independent but are related to each other through the size of the tunneling current
Graphic: Ph.D. thesis: Vratislav Michal
Graphic: Clarke & Wilhelm
Circuit Symbols

## Slide 31: Josephson Junction as nonlinear inductor
Effective inductance depends on the current
Looks like a non-linear inductor: origin of anharmonicity: spacing between energy levels is not the same
  Enables the individual addressing of a single pair of states
  In contrast, in a linear circuit, all states are equally spaced
Image credit: Doug McClure, IBM

## Slide 32: Superconducting Quantum Interference Device (SQUID)
Parallel Josephson Junctions
Magnetic field induces circulating current
Simple analysis: neglect inductance of loop, assume both JJs are identical
The second equation comes from integrating the canonical momentum around the loop (See e.g., Van Duzer & Turner)
If the total current is zero:
Thus applying a magnetic field will induce a current, and consequently tune the inductance

## Slide 33
Slide credit: Doug McClure, IBM

## Slide 34: Coupling to a Transmon
Co-planar microstrip resonator formed by gaps in center conductor
Important to properly choose resonator frequency with respect to transmon frequency (more to come)
Control is achieved by injecting an RF signal from one end
Readout is achieved by looking at either the transmitted or reflected signal
Blais, et al

## Slide 35: Other Transmon Designs
Chow, PhD Thesis
Flux Tunable Qubits
Fixed FrequencyQubits
Current control line
Coplanar microwave resonator

## Slide 36
Slide credit: Doug McClure, IBM

## Slide 37
Slide credit: Doug McClure, IBM

## Slide 38: Derivative Removal by Adiabatic Gate (DRAG) Examples

## Slide 39: Control and Read-out
When the microstrip resonator is detuned from the transmon frequency, interaction with the transmon splits the resonator response into two modes, depending on the transmon state
Sending in a pulse near r enables you to read-out the state either from the phase, or the amplitude
Sending in a pulse detuned from the microstrip resonator but tuned to the qubit frequency rotates the state, but does not make a measurement (there is no information about the state in the reflected signal, the resonator is so far off resonance)
Blais, et al

## Slide 40: I Q Constellation of Measured Signal
https://www.rfwireless-world.com/Terminology/heterodyne-receiver-versus-homodyne-receiver.html
McKay, et al Phys Rev A 96, 022330 (2017)

## Slide 41: Entangling Two Qubits

## Slide 42
Slide credit: Doug McClure, IBM

## Slide 43: Cross-resonant coupling
Frequency switches on coupling
Amplitude controls the gate speed
Phase determines the two-qubit gate
Rigetti and Devoret

## Slide 44: Example IBM Chip Layout
Kandala et al.