## Slide 1: ENHANCING REAL TIME CAPABILITIES OF NANO-RK FOR TELOSB PLATFORM
Devendra Modium
Krishna Priya Kolla

## Slide 2: Problem Statement
Radio Stack and Sensors are very important for functioning of any mote in a wireless sensor network.
Nano RK doesn’t support radio stack and other sensor functionality for TelosB platform
Goal : To enhance Nano RK to provide support for radio transceiver, temperature sensor and light sensor along with power saving mode

## Slide 3: CC2420 Radio Implementation
Telos Rev. B platform has chipcon CC2420 (radio transceiver)
Base Nano RK has the higher level API to send and receive packets
CC2420 is configured using I/O pins and SPI bus.
USART0 module is used in SPI mode to communicate with CC2420
Testcase from HW1 is used to test Radio Stack

## Slide 4: Sensors Implementation
Telos Rev. B platform has SHT11 sensor for temperature and Hamamatsu S1087, S1087-01 photo diodes to sense light
Relevant pins of MCU are configured appropriately to make the Sensors work correctly.
Data sheets and MantisOS are referred for implementation
Incorporated the sensor functionality in NanoRK general device driver model
Testcase from HW1 is used to test Light Sensor

## Slide 5: Power Saving Mode
Telos Rev. B platform has five different power saving modes
LPM3 mode which has CPU off , MCLK off, SMCLK off, DCO off, ACLK on is used for power saving(sleep) mode
Testing is done using LEDs to track the entering and exiting of Low power mode

## Slide 6: Questions ??